## Slide 1: BMWG – Containerized Infrastructure Benchmarking
IETF 109
November 9-13, 2020
Online

## Slide 2: Hackathon Plan
The main goal is to figure out container networking performance impacts by various resource options.
  Related Draft: Considerations for Benchmarking Network Performance in Containerized Infrastructures ​https://tools.ietf.org/html/draft-dcn-bmwg-containerized-infra
  Two main features
    Implementing containerized infrastructure with various network models
    Verifying performance impacts depending on configuration settings

## Slide 3: Hackathon Plan
1st Hackathon at 106 Singapore
  Network technology : User-space vSwitch model
    DPDK / Contiv-vpp
  Verifying CPU allocation using current container orchestration engine
    Kubernetes CPU Scheduler (v1.6.1)
    Compare with CPU pinning technology
      CMK(CPU Manager for K8S)
    NUMA-affinity
Hackathon results were included in our updated draft
  Chapter 6

## Slide 4: Hackathon Plan
This is our 2nd Hackathon
  Using Network model : User-space device pass-through model
    SR-IOV / DPDK
  Verifying huge pages impacts on network performance and resource utilization
    In our draft, Chapter 5;
    “… the container is isolated in the application level and administrators can set huge pages more granular level.
    ..Even if the page size is smaller than the VM, the effect of the huge page is large, which leads to the utilization of physical memory and the increasing number of functions in the host.”

## Slide 5: What got done
Infrastructure Setting
  https://github.com/huyng14/bmwg- container-network
Kubernetes (1 master, 1 worker)
  MULTUS CNI
  CMK for CPU Pinning
  SRIOV plugin with DPDK

## Slide 6: What got done
Data path
  Depending on huge page size, there are different number of virtual address space
    2Mi huge pages = 2,048 pages
    1Gi huge pages = 4 pages

## Slide 7: What we learned
Test Results
  The hugepage size does not affect the network performance
    Ethernet frame is limited to 1518 Bytes
    Just for networking, small size of hugpage is enough
  But we do not measure application process
    Depending on application, performance can be different
Issues
  Out of memory error
    POD access to the non-allocated memory
  Just 1 hugepage size should be tested for each time
    Different configuration of Grub, plugins and K8s should be required for each time
    It takes a lot of time to change configuration, and also high risk to be error!

## Slide 8: What we learned
Future Plans
  Update content of test environment, trouble-shooting and results
  Using other network technologies and benchmarking scenarios for contributing to our draft
    East-West traffic pattern test
      Memif, …
    Kernel based model consideration
      eBPF with variation of resources

## Slide 9: Wrap Up
Team members:
Younghan Kim (SSU)
Hyunsik Yang (SSU)
KJ Sun (SSU)
First timers @ IETF/Hackathon:
Quang Huy Nguyen (SSU)
Vu Dinh Dai (SSU)
Jangwon Lee (SSU)
Hackathon mirror workshop at Busan, South Korea : Collaborated with IPWAVE and I2NSF team (SKKU)